## Slide 1: Existing VHF Systems: Already a problem. Not able to use adjacent channels at close distances.
155.745
155.760
155.775
20KHz Bandwidth
20KHz Bandwidth
20KHz Bandwidth
Overlap
Overlap
Adjacent channels
WideBand
WideBand
WideBand
Joe Kuran Oregon SIEC
15KHz Channel Spacing
15KHz Channel Spacing

## Slide 2: After Narrowband: Still a problem Narrowband channels not usable until wideband users vacate.
155.745
155.760
155.775
20KHz Bandwidth
20KHz Bandwidth
20KHz Bandwidth
Overlap
Overlap
155.7525
155.7675
ANALOG
NARROWBAND
7.5KHz Channel Spacing
Wide Band
Wide Band
Wide Band
11KHz Bandwidth
ANALOG
NARROWBAND
Joe Kuran Oregon SIEC

## Slide 3: After all convert to Narrowband Still some overlay with analog modulation .
155.745
155.760
155.775
155.7525
155.7675
7.5KHz Channel Spacing
11KHz Bandwidth
This represents analog voice with a 11KHz necessary bandwidth
ANALOG NARROWBAND
ANALOG NARROWBAND
ANALOG NARROWBAND
ANALOG NARROWBAND
ANALOG NARROWBAND
Joe Kuran Oregon SIEC

## Slide 4: Convert to Project 25 Digital Phase I Digital Modulation allows tighter packing of channels Still a very minor overlay in the VHF band. UHF band will have no overlay because of 12.5KHz Channel Spacing.
155.745
155.760
155.775
155.7525
155.7675
7.5KHz Channel Spacing
8.1KHz Bandwidth
DIGITAL
NARROWBAND
P25 with C4FM Modulation only requires 8.1KHz Necessary Bandwidth
DIGITAL
NARROWBAND
DIGITAL
NARROWBAND
DIGITAL
NARROWBAND
DIGITAL
NARROWBAND
Joe Kuran Oregon SIEC