## Slide 1: NPSTC RPC Committee
Regulatory Update
David Eierman/Bette Rinehart
Motorola
700 MHz Clearing Status

## Slide 2: 700 MHz Clearing Status
President Bush signed the date certain DTV transition legislation on Feb 8, 2006; Part of S.1932, Deficit Reduction Act of 2005
Law provides for:
  Firm TV clearing date of 02/17/09
  Up to $1B for interoperable communications equipment for public safety

## Slide 3
TV Blocking Public Safety Spectrum
54% Pop’l Totally Blocked
Add’l 16% Pop’l Half Blocked

## Slide 4: TV Protection
Must protect incumbent full power TV stations as outlined in 90.545 until end of TV transition period
Rule of thumb separation of land mobile (LMR) and broadcast TV:
  Co-channel (63/64) = 100 miles
  Adjacent channel (62/63/64/65) = 60-80 miles
  Co-channel (68/69) = 100 miles
  Adjacent channel (67/68/69) = 80 miles

## Slide 5: TV Short-Spacing
Short-spacing opportunities may exist
  Terrain factors
  Directional antennas
  Using minimum possible ERP/Antenna Heights
Rules provide certain avenues
  Engineering Studies
  Consent of Incumbent Broadcaster
Can also file waiver
  Examples:
    Granted Access Spectrum waiver
    Pending New York State waiver